## Slide 1
Home Control Solution - DYI
- Project Proposal -
Sponsor: Cẩm Châu
Students: Hai Nguyen

## Slide 2: Executive Summary
Designed to be a fully functional, resource independent system that incorporates energy saving designs.
All-in-one solution with modern User experience with no limit on security, energy control, surveillance observing, voice recognition ,face recognition, finger print recognition…
User can benefit from:
  A sensor network that is linked to a central server
  Motion sensors to monitor motion in a given space or room
  Analyze power usage by capturing real-time power data
  Real-time monitoring of water level and water flow via sensors
  Open-source and low cost system
  Mobile app and webpage to access

## Slide 3: Introduction
Sensor nodes provide a real-time acquisition of data and wirelessly transmits that data to the server.
Interfacing with four sensors (ambient light, humidity, temperature, and motion sensing) in a node.
Open-source, flexible and expandable.
Low component cost, easy-to-use, low energy required.

## Slide 4: Scope
In this proposal, we will describe the features of our solution
We will then outline some risks and dependencies and how we will address those risks.
Finally, we will outline the per room cost and overall project cost.

## Slide 5: Proposal Format
System Overview
Overview of the HiNode platform & Sensors
Overview of the Outputs
Communication Protocol
Documentation
Risks and Dependencies
Predictable Cost

## Slide 6: System Overview
Node diagram of a wireless sensor network

## Slide 7: Overview of new design of wireless sensor/control node network and new node platform (HiNode)

## Slide 8: HiNode
A HiNode based on:
  Pro Mini atmega328 5V 16M, L*W*H:33mm *118*6mm
  NRF24L01+ 2.4GHz Antenna Wireless Transceiver Module
Compatible with Arduino IDE and libraries.
Enable both digital and analog multiple sensor acquisition.

## Slide 9: Pro Mini atmega328 5V 16M
L*W*H:33mm *118*6mm

## Slide 10: NRF24L01+ 2.4GHz Antenna Wireless Transceiver Module

## Slide 11: HiLink
HiNode
232RL USB Download Cable To Serial Adapter Module For Arduino USB TO 232
Communicate with the server through USB

## Slide 12: Ambient Light Sensor
A light-sensitive electronic component that can sense environment’s light level.
Output voltage value corresponding to the light level.
Use the AMBI light sensor from Modern Device Company.

## Slide 13: Motion Sensor
Use PIR (Passive Infrared) sensor. Detecting motion by using IR signal.
Use the Zilog's ePIR sensor. Provides superior sensitivity and stability.
Interface with HiNode through serial communication.

## Slide 14: Humidity/Temperature Sensor
Used for sensing the temp. and humidity of the environment.
Use the DHT-22 sensor which combining two sensors in one package.
Low-cost and easy to use by using an open-source library.

## Slide 15: Water-level Sensor
Use ultrasonic sensor.
It’s used for measuring distance by using ultrasonic wave.
Use the PING)))™ ultrasonic sensor from Parallax.
Low –cost, easy to use, and accurate.

## Slide 16: Power Monitoring
Measuring current flowing in the service conductors using a clamp on current transformer (CT).
Capable of measuring up to 400 amps.
The output will be connected to the HiNode to allow scaling and power calculation.

## Slide 17: Water Flow Sensor
Use Hall-effect sensor. Rolls when water flows through it.
Send pulses to HiNode at a frequency of 0 to 450Hz.
These pulses will be counted to find out the amount of water flowing through.

## Slide 18: Soil Moisture Sensor
Use a two-stake sensor attached to analog ports on HiNode.
These sensors can be two galvanized nails or screws separated by a given distance.
Calculate the soil moisture based on the resistance.

## Slide 19: Power Supply
Beside, 220V AC wire in wall, the project need 12V DC power line in wall, then will support the power:
  5V DC
  3.3V DC

## Slide 20: Overview of Outputs - Dimming Lights and Outlet -
Use Relay from HiNode to control the outlet
Cost is coming down while reliability is going up.
Need 12V DC power line for all node. (sensor and Control)

## Slide 21: Overview of Outputs - Blinds and Motors-
Blinds:
Controlled by a sensor node.
Can set min and max point to open and close the blind
Water pump/motor:
Use a motor with HiNode controller
Operate based on data from the soil moisture sensor

## Slide 22: Communication Protocol
When a node wants to communicate with another node, the data could be packaged in the following manner:
Frame | Route | Action | Data | End of package
Route | Path of the transmission
Action | What the sender is going to do
Data | Data to send to the destination
End of package | Termination the transmission

## Slide 23: Communication Protocol
Central Node
ID =1
ID=2
ID=3
Node 1 send map | Route |  |  | Action | Data |  |  | EOP
 | 0x02 | 0x02 | 0x03 | M | 0x02 | 0x02 | 0x01 | 0xFF
Node 1 send request | Route |  |  | Action | Data | EOP
 | 0x02 | 0x02 | 0x03 | R | T | 0xFF
Node 3 send data | Route |  |  | Action | Data |  | EOP
 | 0x02 | 0x02 | 0x01 | D | T | Value (1 byte) | 0xFF
Example: Getting temperature from node ID = 3

## Slide 24: Documentation
Will include all theory, assembly, alternatives and modifications of the project.
Links to all online resources will also be included.
Open-source documentation.
Invites revisions, refinements and further support from the open-source community

## Slide 25: Risks and Dependencies
Motor for Composting Toilet: Automation is not recommended by manufacturer.
Minimum and maximum torque/speed for the composter’s tines is unknown.
Blind motors: The size, weight and action of the blind is undefined. This increases the complexity of choosing an appropriate motor and it's method of control.
The number of sensor nodes needed could change. An increase cost is possible.

## Slide 26: Risks and Dependencies
The ultrasonic sensor may suffer from water splash damage and humidity buildup.
Water-flow sensor selected has durability concerns. The inlet size of 1/2” may not suffice for measuring a household. An alternative sensor is available for $80-$300.
Assembly materials and sensor enclosures will be determined later. The cost for both in this document is only an estimation.

## Slide 27: Predicted Cost
Part Name | Part Number | Manufacturing | Vendor | Price per Part | 
HiNode Wireless PCB | HiNode V5 Kit | JeeLabs | www.moderndevice.com | $22.50 | 
DHT22 - Humidity/Temp Sensor | SEN-10167 | Aosong Electronics Co.,Ltd | www.sparkfun.com | $8.96 | 
Ambient Light Sensor | AMBI Light Sensor | Sharp | www.moderndevice.com | $4.47 | 
Motion PIR Sensor | SEN-09587 | Zilog | www.sparkfun.com | $10.76 | 
Ultrasonic (Water Level Sensor) | SEN136B5B | Seeed Studio | www.robotshop.com | $15.00 | 
Water Flow Sensor | POW110D3B | Seeed Studio | www.robotshop.com | $9.50 | 
SuperSocket - Wall Receptacle Module | SR227 | X-10 | www.x10.com | $15.99 | 
Decorator Dimmer Switch | x10_ws12a | X-10 | http://www.x10.com/products/x10_ws12a.htm | $19.99 | 
Project Component Cost

## Slide 28: Predicted Cost
Sensor Node Package | Part Number | Manufacturing | Vendor | Price/ Part | 
HiNode Wireless PCB | HiNode V5 Kit | JeeLabs | www.moderndevice.com | 22.50 | 
DHT22 - Humidity/Temp Sensor | SEN-10167 | Aosong Electronics Co.,Ltd | www.sparkfun.com | $8.96 | 
Ambient Light Sensor | AMBI Light Sensor | Sharp | www.moderndevice.com | $4.47 | 
Motion PIR Sensor | SEN-09587 | Zilog | www.sparkfun.com | $10.76 | 
 |  | Total Price Per Sensor Node: |  | $46.69 | 
Deployment Costs | Estimated Nodes | Total Cost
Estimated cost of sensor node deployment | 16 | $747.04
Sensor Node Cost
Estimate Deployment Cost

## Slide 29
Lower Floor

## Slide 30: Upper Floor

## Slide 31: Predicted Cost
Research and Development Cost | Purpose | Total Cost
Budget | Component purchases for design and testing | $500.00
Research and Development Costs
The predicted cost does not reflect the cost of the motors nor the interface materials for the motors.
Estimate of $300 to $400 for the composting toilet DC motor.
The price for the blind motor is still unspecified

## Slide 32: Conclusion
With this wireless sensor network, users can access information about temperature, humidity, light, and occupancy in a room, water level in a container, and power usage via an interface to a central server without directly going to the sensors to read information.
Users are able to control outputs such as motors and light levels wirelessly.
The system itself is power-efficiency and cost effectiveness.
Assist the home owner in reducing energy consumption as well as making the home more energy efficient through automation.

## Slide 33: Q & A

## Slide 34: Communication protocol (backup)
Frame | Route | Action | Data | End of package
Action | What the sender is going to do
M: Sender wants to send map to the destination.
R: Sender wants to send request to the destination.
D: Sender want to send data to the destination

## Slide 35: Communication protocol (backup)
Frame | Route | Action | Data | End of package
Data | Data to send to the destination
Depending on the Action:
Action is M: Data contains the route telling the destination node how to get back the sender.
Action is R: Data contains one byte standing for names of sensors the sender is requesting (H, T, L, O, W, Z).
Action is D:
  From sender: Data contains the command from server to control the outputs.
  From destination node: Data contains values from sensors.